## Slide 1: Generating FPGA-based In-line Accelerators
By: Maysam Lavasani
Under supervision: Prof. Derek Chiou
Notes: Thanks for coming to my proposal session. The title of my proposal is

## Slide 2: Committee
Derek
Patt
Andreas
Mattan
Jacob
Eric
(Pingalli?)

## Slide 3: Outline
Motivation and background
Gorilla
  Architecture view
  Automation view
Case studies and experimental results
Plan for future

## Slide 4: Benefit of customization
Notes: This graph shows energy efficiency of 20 different fabricated chips which have publication in ISSCC before 2000. The graph is not implementation of single application using different substrate. The efficiency is based on the max throughput of chip among different benchmarks. The operation is basic ALU operation for that particular chip.

## Slide 5: Internet core routers
  Multi-chassis system
  322Tbps aggregate bandwidth
  Download the entire Library of Congress content < 1 sec
  Simultaneous video call for everyone in China
  Almost one instruction/ingress bit
  Almost one memory access/bit
CISCO CRS-3 (Carrier Routing System)
1GIPS < 0.1Watts
Indepnent threads
Notes: Internet routers are a successful practice in customization with respect to computation, memory, and IO resources. Lets briefly look at the Internet routers architecture which is my role model in this research.
The highest capacity router I could find
  2.73 Watts per Gbps (total power)
  Compute power : 35%

## Slide 6: In-line acceleration in core routers
Throughput machines
IO intensive
Irregularity in control-flow
High bandwidth random memory accesses
Customization at various levels
  Network interfaces
  Inter-core communication
  Memory interfaces
  Core architecture
Fast-path accelerator
Interconnect
Cores
Memory
Slow-path processor
Metro NP (CRS-1 2007)
                188 32-Bit embedded RISCs
                96Gbps bandwidth
                5xQDR+9xFCRAM+2xTCAM channels
Notes: We show a simplified view of a router architecture.
Fast-path accelerator = Data-plane accelerator = In-line accelerator
FCRAM: Fast cycle RAM: more aggressive pipelining on handling DRAM commands

## Slide 7: Research highlights
FPGA-based high-end network processors?
Generalize such technique to other applications?
Notes: Like many other researchers my reasearc can be summarized

## Slide 8: FPGAs
Comparing FPGA vs Custom CMOS and the Impact on Processor Microarchitecture, H. Wong et al, FPGA 2011
Notes: Unlike ASICs, FPGAs are a highly flexible substrate for specialization. However they have the area and timing overhead of building logic, memory, and interconnects through programmable components.
An important question is whether the benefit of customization can out weight the FPGAs overhead?

## Slide 9: Thesis statement
FPGA-based resources, if used with efficient overlay microarchitecture, can improve the throughput and/or energy efficiency of a class of networking and big data applications.
I present a template based methodology for generating FPGA-based accelerators and showcase the methodology by accelerating targeted applications.
Notes: This can be done using (i)Automatic Slicing the applications into fast path/slow (ii)a template based design process which enables design space exploration as the first class character in the process for designing the fast path.

## Slide 10: Our focus
FPGA-based accelerator
In-line accelerator
High-level programmable
Notes: There are research on FPGA accelrators, In-line accelerators, and HLS. We focus on the intersection of these three

## Slide 11: Targeted Applications
Networking
  IPv4/IPv6 routing, MPLS switching
Datacenter applications
  Memcached, Kmeans, Page rank, Word count
The common characteristic of such applications are
Input/Output data through system NIC
Hot computational kernels
Irregular data parallel
  Control flow
  memory access
Notes: Networking and data center applications are an important class of applications which can use specialization for improving the energy. Like many other data parallel applications such applications can utilize large number of hardware execution contexts. Since specialization enables better ratio of required resources(both transistors and energy) over unit of throughput we can increase number of execution units for a particular aggregate resource budget and consequently achieve better efficiency.
Our targeted applications have two important characteristics which differentiate them with other types of data parallel architectures, (i)irregularity and (ii)requirement to access shared resources.

## Slide 12: Contributions
Gorilla methodology/toolset
  Template based design methodology
  Functional parallelization templates
  HLS optimizations for fused operations
Showcasing Gorilla
  Generating core network processors
  Generating big data accelerators
  Comparing energy efficiency against GPP
Notes: Design space exploration as first order requirement
The process is not completely automated though.

## Slide 13: Evaluation methodology
Performance: all accelerators realized at Verilog level
  Throughput
  Energy efficiency: Energy/operation
Productivity: development time

## Slide 14: FPGA/CPU/GPGPU comparison
 | CPU based solution |  | GPU based solution | 
Application | Throughput | Energy efficiency | Throughput | Energy efficiency
Routing IPv4 | 16x | 100x | 4x | 
Memcached | 10x | 50x |  | 
This translates into almost 50% power saving at system level
Notes: Unfortunately I don’t have the performance numbers for all targted applications across all these three platform.
But thanks to other people publications I am comparing the FPGA-based solution I built with CPU and GPGPU based solution from related works.

## Slide 15: Architecture related work – Overview
 |  | Application |  | In-line features |  | Programmablity | 
 |  | Layer 2&3 | Above layer 3 | Slow path coupling | Zero-copy packet | FPGA-based | High level programmable
NetFPGA |  |  |  |  |  |  | 
L3+ FPGA networking |  |  |  |  |  |  | 
Network processors |  |  |  |  |  |  | 
Networking with General purpose hardware |  |  |  |  |  |  | 
Smart NIC |  |  |  |  |  |  | 
Integrated NIC |  |  |  |  |  |  | 
Datacenter Acclerator chip |  |  |  |  |  |  | 
TCP slicing |  |  |  |  |  |  | 
Magilla |  |  |  |  |  |  | 

## Slide 16: Automation related work – Overview
 |  | Data flow FIFO interfaces | Offloading / shared state | Pipeline synthesis | Parallelization template | Architecture decoupling | HLS
Vivado |  |  |  |  |  |  | 
Architectural HLS |  |  |  |  |  |  | 
HGL |  |  |  |  |  |  | 
FPGA Overlay |  |  |  |  |  |  | 
Synch Dataflow on FPGA |  |  |  |  |  |  | 
Green droid |  |  |  |  |  |  | 
Legup |  |  |  |  |  |  | 
Magilla |  |  |  |  |  |  | 

## Slide 17: Gorilla: Template based design

## Slide 18: Gorilla Methodology
Domain expert writes in stylized C (domain code)
Hardware designer writes parameterized hardware components (hardware template)
  Parameters may be values or code
  Functional parameters
    E.g., IPv4 code or IPv6 code
  Performance parameters
    Number of threads, packets in flight, scheduling policy
Tools automatically
  Merge domain code with hardware templates
  Explore the design space to meet the design constraints
Sharp contrast with C-to-gates approaches
  Gorilla uses predesigned template for the target hardware

## Slide 19: Gorilla Design Process
Domain code
Select a hardware template
Library of hardware templates
Functional parameters specialization
Find initial seeds for performance parameters
Performance evaluation
Architectural enhancement by changing parameters
No
Yes
Hardware designer adds new template or change the current template
No
Performance parameters specialization
Work loads
Met goals?
Performance goals
Possible?
Yes
Manual step
Automatic step

## Slide 20: Architecture

## Slide 21: Execution Model
A single processing kernel is applied on each input data element and generates an output data (infinite loop)
kernel is modeled as a set of processing steps

## Slide 22: Domain Code - Programming Model
Each processing step (G-block)
  Arithmetic/logic operation on program input and context variables (globally visible to all functions)
  call to special purpose offload engines
  Explicit, computed jump to next step
instr_addr_t IP_CLASSIFY()
{ IP_protocol_t wordx;
//Lookup the destination address
Dport = LOOKUPX.search(Da);
//Read the TTL and Chksum fields
wordx = MEMX.read(PP, TTL_WORD);
TTL = wordx.TTL;
Chksum = wordx.CHKSUM;
TTL = TTL – 1;
Chksum = Update_chksum(Chksum);
switch (TTL == 0) {
case OK: Next_step = NP_INSTR_EMIT;
default: Next_Step = NP_INSTR_EXCEPTION;
}
}

## Slide 23: A Programmable Engine
Context memory
Control state
Offload engine
Off-chip Memory
Engine

## Slide 24: Scaling Throughput
Engine
Multiple engine contexts
  Multi-threaded engines
  Multiple engines
Contexts increase performance until an offload engine becomes the bottleneck
Control state
Offload engine
Off-chip Memory
Context memory

## Slide 25: Pipelined Engines
Multithreading the engines and engine duplication are not the only ways for increasing the throughput
Pipelining the engine is possible providing
  No backward jumps between processing steps
  Access to an accelerator is restricted to a given pipe stage
Pipelining has sometimes lower overhead than other solutions
  No thread management overhead
  No duplication overhead

## Slide 26: Packet Processing Hardware Template

## Slide 27: General purpose cores collaboration
General purpose core
Coherent memory system
$
General purpose core
$
Engine
Off-load engine
Off-load engine
Configuration/Status registers
Compute engine
Stream in
Load balancer
Stream out
Load merger
In-line accelerator

## Slide 28: Automation view

## Slide 29: Chisel

## Slide 30: Leg up

## Slide 31: Engines
Engine
Offload engine
Input data
Input valid
Input ready
Output data
Output valid
Output ready
Input control
Output control
Request
Reply
FrameIO
FifoIO
OffloadIO
Notes: Mix this with Chisel code

## Slide 32: Intra engine parallelization patterns
Pipelining
Multithreading

## Slide 33: Engine generation
Val lookup = PIPED_ENGINE(“trieLookup.c”)
Val ipv4Engine = MT_ENGINE(“ipv4.c”, num_of_threads)

## Slide 34: Gorilla Compilation Process
Written in ANTLR

## Slide 35: Multi-engine parallelism patterns (I)
Course grain pipeline
Replication

## Slide 36: Multi-engine parallelism patterns (I)
Offload
Offload filter

## Slide 37: Parallelization patterns – Replication
Val headerProcessor =
OFFLOAD(REPLICATION(module=cluster,
count=num_of_clusters, loadBalancePolicy=roundRobin), QDRlookup, arbitrationPolicy=roundRobin)

## Slide 38: Parallelization patterns – Coarse grain pipeline
  val packetForwarder =
  CG_PIPE(disassembler,
  SEQ_REORDER(headerProcessor),
  reorder,
  assembler);

## Slide 39: Kmeans accelerator
Val KmeansPipe =
PIPELINED_ENGINE(“kmeans_pipe.c”)
Val KmeansDataFeed =
MT_ENGINE(“Kmeans_control.c”, 1)
Val KmeansCoresCluster =
REDUCE(REPLICATE(OFFLOADER(
KmeansDataFeed, KmeansPipe), coreCounts), kmeansReducer)
Val Kmeans_accl =
CG_PIPELINE (Streamer,
LambdaCoresClusters, Streamer)

## Slide 40: Preliminary results

## Slide 41: Routing experimental Results - 100MPPS on Virtex-6 VHX380T

## Slide 42: Board Implementation
Gorilla-generated network processor
IPv4 only on ML605
  Xilinx Virtex-6 XC6VLX240T
  Emulate QDRs with accurate timing in BRAMs
16-3-2 configuration delivers 100MPPS
  Most of the logic running at 100Mhz
  Consistent with simulation results
Random packet generator and statistics collector
Core power (excluding the I/O) less than 4 watts
Notes: A picture from board required here

## Slide 43: CPU/GPGPU/ASIP comparison
Core router NP on a single FPGA
  Xilinx Virtex-7 VHX870T FPGA
  200MPPS throughput (100 Gbps)
    More than 6x performance of 32 Nehalem cores
      Routebricks[SOSP09]
    Twice the performance of 8 Nehalem cores, 2 Nvidia GTX480 GPUs
      Packetshader[Infocom10]
    Fastest network processor – 400MPPS

## Slide 44: Memcached evaluation

## Slide 45: Memcached Get throughput

## Slide 46: Accelerated Memcached throughput

## Slide 47: K-means Results

## Slide 48: Future work
HLS optimizations
Full integration between Chisel based HW generator and HLS compiler
Complete implementation of page rank and word count
Generating some intermediate results from deign space exploration to undestnad the performance

## Slide 49: Gaunt chart
Task/Month | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
HLS optimizations |  |  |  |  |  |  |  |  |  | 
Chisel-HLS integration |  |  |  |  |  |  |  |  |  | 
Implement Page rank and word count |  |  |  |  |  |  |  |  |  | 
DSE |  |  |  |  |  |  |  |  |  | 
Thesis |  |  |  |  |  |  |  |  |  | 

## Slide 50: Courses
UT Courses | Instructor | grade
SOC design – Fall 08 | Dr. Jacob Abraham | A
Comp Arch: User/system interplay – Spring 09 | Dr. Mattan Erez | A
Parallel systems – Spring 09 | Dr. Calvin Lin | A
Parallel comp arch – Fall 09 | Dr. Derek Chiou | A-
Communication systems – Fall 09 | Dr. Yin Zhang | A
Microarchitecture – Spring 10 | Dr. Yale Patt | A-
Comp Arch: Parallelism and Locality – Fall 10 | Dr. Mattan Erez | A

## Slide 51: Related publications
Maysam Lavasani, Larry Dennison, and Derek Chiou. "Compiling High Throughput Network Processors." Proceedings of the 20th ACM/SIGDA International Symposium on Field-Programmable Gate Arrays, Monterary, CA, Feb, 2012.
Maysam Lavasani, Larry Dennison, and Derek Chiou. "Methodology for Leveraging Reconfigurability in Domain Specific Languages." The First Workshop on the Intersections of Computer Architecture and Reconfigurable Logic (CARL 2010), December 2010

## Slide 52: Thank you

## Slide 53: Packet Header Processing

## Slide 54: Experimental Results - 200MPPS on Virtex-7 VHX870T

## Slide 55: Understanding the performance (work in progress)

## Slide 56: Simplified performance projection
Assumptions (Engines limit performance)
  Enough parallelism
  Ideal inter engine interconnection
  Ideal load balancer
  Enough memory bandwidth
Performance = P0 x C x P x M x F
C: In-cycle operations compaction factor
P: Intra engine parallelism
M: Multiple engine parallelism
F: Cycle time

## Slide 57: Area efficiency/Resource balance
Smaller engines - larger M
  Application specific data path width
  Application specific functional units
  Applications specific Register file
  Application specific level of threading/pipelining
Resource imbalance - smaller M
  Large number of required double-precision units
  Large amount of on-chip memory

## Slide 58: Methodology
Identify contributions to performance
  Timing model for a sea of simple cores
    multi-threaded 5-stage pipeline cores
    connection through NOC
  Gorilla type architecture on FPGA

## Slide 59: Performance contributors – FPGA tax
Frequency tax
Area tax

## Slide 60: Performance contributors – Intra-engine Benefits
Customized data path
  Wide combinational logics
  Chained combinational logics
Register access
  Distributed
  Large
Customized pipelining
Simplified front-end
  Multi-threading + no branch prediction

## Slide 61: Performance contributors – Inter-engine Benefits
Pushing data elements vs pulling
Multi-port to offload engines
Through memory operations
Customized communication
Small engines - larger engine counts

## Slide 62: Coherent fast-path acceleration

## Slide 63: Execution model

## Slide 64: Memcached

## Slide 65: Memcached Internal

## Slide 66: Memcached performance results

## Slide 67: Related works

## Slide 68: Related works categories
Computation model
System level research
Architecture level research
FPGA related research
CAD related research
Notes: This is an FPGA implementation of an interesting application at system level using different architectural techniques and CAD techniques.So naturally it has many related works.

## Slide 69: Show casing template-base design
Magilla
  Difference:
    Not only engines but also accelerators/pre-processor/post-processor can be programmed using Gorila instructions
    Multiple engines/Engines clustering
    Mulitple frequency domain
Jason Cong DATE 2012 and other StreamIt on FPGA
  Similarity: Design space exploration for both fine-grain as well as coarse-grain architecture parameters
  Different because of shared data

## Slide 70: Show casing template-base design (continue)
Scott Hulk ...
  Simmilarity: Data parallel mostly by pipelineing
  Difference: no multithreading and shared state
NISC
Convey

## Slide 71
Greendroid
  Different application
  Different substrate

## Slide 72: Smart/Integrated NIC
Smart NIC
  Batching
  Multiple queues (Per core queue) –RSS
  Segment offloading – NIC can packetize messages
Integrated NIC
  On-loading (Rienhart paper)

## Slide 73: Generalizing the In-line acceleration – FPGA based application accelerator
SQL
Honeypot
Memcached accelerator
FPGA based machine learning for search
Other paper from HP lab referenced by Memcached FPGA2013

## Slide 74: Generalizing the In-line acceleration – NP based
ANCS 2009 – Web server acceleration
Open onload

## Slide 76: Understanding the contribution to performance
Eric's paper

## Slide 77: Primitive interface bundles
Source
Sink
valid
ready
data
class FifoIO[T <: Data] () (dataType: => T) extends Bundle {
val valid = Bool(Output)
val ready = Bool(Input)
val flit = dataType
}
//More code …
source.io.output <> sink.io.input
valid
ready
data
valid
ready
data

## Slide 78: GPP-ASIC gap
Reconfigurable components for application-specific processor architectures, Nolll, T et al.
Five orders of magnitude gap

## Slide 79: GPP-ASIC gap
Understanding the source of inefficiencies in general-purpose chips, ISCA 2010, Horowitz. M. et al.
Notes: Pentium 4 with SSE 2.8Ghz

## Slide 80: Fast path realization process
Fast path realization using hardware templates
  Combining application code with templates
  Balance between different parallelization
    Engine level
    Thread level
    Pipeline level
  Through memory engines
Slicing the application into fast path/slow path
  fast/slow path synchronization/communication

## Slide 81: Top level design process
A canonical architecture containing both general purpose cores(GPCs) and special purpose cores(SPCs) is proposed.
A program is sliced between hot path running on SPCs and cold path running on GPCs. The hot path is sliced further into state-less and state-full components.

## Slide 82: Synthesis process
For designing the SPCs a class of functionality independent templates for throughput oriented processing engines are proposed. Engine template has tunable degree of specialization in terms of instruction supply, data path, and context memory is proposed. It also has tunable degree of parallelism i.e multithreading, pipelining. Also coarse grain templates for building architectures by composing processing engines are proposed.
Such flexibility (i) splits the design effort between domain expert programmer and hardware designer (ii) enables the design space exploration tool to find virtually the least expensive solution for a given application with specific performance goals.

## Slide 83: Design space exploration and refinement
Although there are several languages for hardware design a language is proposed with the main focus on efficient design space exploration. Also the appropriate tools are developed for compiling the templates into the hardware as well as exploring the design space for enhancing the template architectures.

## Slide 84: Related work

## Slide 85: Related work layout
Although we want to focus on hybrid GPC, SPC architectures for a particular application class (networking and data center) on particular HW substrate (FPGA), in order to compare our work with relative work, a broader view at SPC design is presented.

## Slide 86: Hybrid GPC/SPC design disciplines for data parallel applications
Parallelization
  Parallelization model
  Dependency, shared state, and ordering
Architecture
  GPC/SPC HW coupling model
  SPC HW substrate
Design automation
  SPC course grain architecture
  SPC mapping
  SPC fine grian synthesis/programming
  SPC refinenment

## Slide 87: Parallelizon models
  Transaction level
  Producer/consumer level
  Fine grained data level
  Slicing (special class of pluralization hardware resources are different (asymmetric multi-core or GPC/SPC))

## Slide 88: Application slicing model
SPC is acting as an off-load component for GPC - encryption coprocessor
GPC is acting as an exception path for SPC - router
GPC is acting in pipeline fashion along SPC - Is this GPU?
Combination of above

## Slide 89: GPC/SPC coupling model
Coupling level
core level
chip level
board level (FSB)
system level (PCI-X)
*Data path level
Coupling mechanism
  Messaging
  Shared memory

## Slide 90: SPC synthesis/programming
Multi-engine architecture
  multi-engine composition
    producer/consumer engines
    parallel engines
    state-less/state-full engines
    mem access engines
Engine architecture
  data path synthesis
    pipelining
    split-pipelining
    multithreading
    combination of above
  control synthesis
  engine programming

## Slide 91: SPC HW substrate
Instruction based (ASIP)
FPGA
Patching
No programmability

## Slide 92: Related work (focus on parallelization and mapping)
Project | Target application | Slicing model | Programming model | Coupling model | SPP synthesis | SPP HW substrate
StreamIt |  |  |  | N/A | N/A | FPGA

## Slide 93: Related work (focus on architecture only)
Project | Target application | Slicing model | Programming model | Coupling model | SPP synthesis | SPP HW substrate
ReMap |  |  |  | MP | N/A | FPGA

## Slide 94: Related work (focus on synthesis only)
Project | Target application | Slicing model | Programming model | Coupling model | SPP synthesis | SPP HW substrate
NISC | Embedded | N/A | N/A | N/A | single engine -automatic micro code generation | N/A

## Slide 95: Related work (focus on architecture and synthesis)
Project | Target application | Slicing model | Programming model | Coupling model | SPP synthesis | SPP HW substrate
Green droid | Mobile | Automatic | Implicit | MP,L1 | single engine- state machine | ASIC

## Slide 96: GPC/SPC systems in action
Router
CPU/GPU

## Slide 97: Our project

## Slide 98: FlitIO
Source
Sink
valid
ready
data
FifoIO
Class FifoIO[T <: Data] (FlitType: => T) extends Bundle {
val valid =
val ready =
val flit =
}

## Slide 99: Interfaces in Chisel
class PushIO extends FifoIO
class OffloadIO[T <: Data]
(offloadType: => T) extends Bundle {
val req = (new PushIO()) {offloadType}
val rep = (new PushIO()) {offloadType}.flip
}

## Slide 100: Outline
Methodology
  Gorilla: A methodology for designing a class of data parallel accelerators using reconfigurable hardware (and maybe more)
Applications
  Core Router
  Memcached Accelerator
  Open flow switch
  Deep packet inspection
  Exotic applications

## Slide 101: Gorilla Methodology

## Slide 102: Gorilla objective
Decouple the performance related programming (by hardware designer) from functionality related programming (domain programmer)
  Give the right job to the right person
Enable design exploration from ground up by using highly parametrized hardware templates
  Makes the hardware programmer job harder?
Give necessary tools to architect to not only reuse the hardware modules but also the architectural enhancement techniques
  Makes the hardware programmer job easier

## Slide 103: Gorilla overview
A highly parametrized template architecture (canonical architecture) will be designed by a performance savvy programmer (hardware designer) for a class of applications. It will be specialized later using domain code by domain expert programmer.
The template parameters consist of functional and performance parameters
  Functional parameters enable us to specialize an architecure for particular application.
  Performance parameters enable us to commit to a specific parameter at the late stages of the design to meet performance constraints (Power, Latency, Throughput, and Area.)

## Slide 104: Does hardware design process still need improvement?
For many applications customized hardware has a meaningful performance difference with software+general purpose hardware but NRE charge and lack of programmability is an obstacle for using customized hardware except for big markets with well established standards
  Design cost is a large part of NRE
  Many design efforts in a particular project is thrown away and not used for next projects
  Constraints like power and routablity has become more important and they can't be evaluated without having low level information (post synthesis)

## Slide 105: Why current tools/methods are not enough?
SystemC/TLM - More about simulation feasiblity and simulation performance
Bluespec - Does not include architectural enhancement features, though it can be used as a substrate for Gorilla.
HLS - Quality of the hardware is not suitable for serious applications
ASIP - Flexiblity for changing instructions. Lack of macro level architectural enhancent.
NISC - building control store for a given datapath for single core only. We want to even improve the datapath. Also we want to improve the hardware at multiple processing engines.
Convey/ROCCC - No macro level customization and architectural enhancment

## Slide 106: Architecture level description of hardware rather than RTL
Defining the (synthesizable) hardware modules which process data units at course level
Keep modules parametrized for
  Reuse (Not just the hardware component but also the architectural technique)
  Architectural exploration for meeting design constraints
  Specialization for a particular application
  Module level throughput (frequency) tuning
    DVFS enabled architecture from ground up

## Slide 107: Abstract hardware modules: SPM/CRM
A Gorilla SPM (Stateless Processing Module) is a hardware component which can process the input data and generates the output data. SPM is stateless, meaning that previous processings do not affect consequent processing through the change on internal SPM resources.
A Gorilla CRM (Common Resource Module) is exactly like SPM except that it might contain logically/physically shared resources.

## Slide 108: Modules
SPM
CRM
Input data
Input valid
Input credit
Output data
Output valid
Output credit
Input control
Output control

## Slide 109: (some) Parallelism patterns for SPMs

## Slide 110: (some) Parallelism patterns for SPMs+CRMs

## Slide 111: (some) Parallelism patterns for SPMs+CRMs

## Slide 112: (some) Parallelism patterns for SPMs+CRMs

## Slide 113: Input to Methodology
Hardware templates including canonical architecutre for a set of applicaitons
Domain code
Work loads
Performance targets
Architectural enahancment library

## Slide 114
Domain code
Select a canonical architecture
Library of templates
Functional parameter specialization
Initial seed for performance parameters
Library of architectural enhancements
Performance evaluation
Meet goals?
architectural enhancmenet search
Performance goals
No
Yes
Found?
Enhance Architecture
Work loads
Hardware designer adds either new template or new architectural enhancement
No

## Slide 115: Modules data access
Through registers
Through input memory and output memory
Through input/output memory (in-place compuation)

## Slide 116: Execution substrate
Processing of the input data by SPM can be done by:
Customized pipelined hardware
Customized multithreaded state machine
Genralized datapath with/without instruction memory

## Slide 117: Infrastructure modules
Load balancer/Load merger
Scheduler
Arbiter
Reorder Queue
scratchpad memory
Interface wrappers

## Slide 118: Automatic architectural enhancemnet
A generalized form for design space exploration
  Intra module: One code should be able to run on any SPM execution substrate and translation is done automatically
  Inter moules: Moving code between modules
  Tuning sizing parameters: Number of threads, processing engines, ...
  Structural: Next example

## Slide 119: A sample architecture
A
B
100Mhz

## Slide 120: A sample architecture enahncment
Arch_enhancement BOOST_SOURCE_FREQ_DUPLICATE_SINK_MODULES
Given A{SPM} -> B{SPM} =>
A_new := A; //A_New is the same type as A
B1_new := B;
B2_new := B;
A_new<frequency=2*A:frequency>;
A_new ->lb::Load_balancer(size =2);
lb.out[0]->ra0::Rate_adapter->B1_new;
lb.out[1]->ra1::Rate_adapter->B2_new;
A.in => A_new.in;
B.out => merge[B1_new.out, B2_new_out];

## Slide 121: A sample architecture
A_new
B0_new
B1_new
lb
200Mhz
100Mhz

## Slide 122: A sample architecture
A::Fetch <code = "fetch.c", width=1>;
B::Decode <code="ARM_decoder.c", width=1>;
A -> B; //same as A.out -> in.B;
A,B interface : 32 bit communication through registers
A
B

## Slide 123: A sample architecture
A::Ethernet_checker<code="Eth_chk.c">;
B::MPLS<code="MPLS_proc.c">;
A -> B; //same as A.out -> in.B;
A, B interface: Memory based FIFO
A
B

## Slide 124: Gorilla methodology example: An out of order processor
Template <...> Core (...)
Icache -> Fetch -> Decode;
Decode-> Rename_Reg -> in.Exec;
ROB.reg_commit -> Rename_Reg ;
Exec.out -> exec_retire.ROB;
Exec.lsu <-> Dcache;
Dcache <-> mem_commit.ROB;

## Slide 125: An out of order processor (continue)
Template <...> Exec (...)
in -> Dispatcher;
Dispatcher.add -> RS_add -> Broadcast_bus;
Dispatcher.mul -> RS_mul -> Broadcast_bus;
Dispatcher.lsu -> RS_lsu -> Broadcast_bus;
Broadcast_bus -> out;
RS_add <-> FU_add;
RS_mul <-> FU_mul;
RS_lsu <-> lsu;

## Slide 126: Methodology for constructing the methodology
Desiging serious applications and learn from that

## Slide 127: Gorilla Applications

## Slide 128: Why focusing on data center and networking applications?
Using specialized hardware is beneficial because of high throughput requirement
Loosely coupled accelerators limit the performance benefit due to communication overhead - In-line accelerators does not have the processor/coprocessor communication overhead

## Slide 129: Applications
Network processor
  High throughput
  Power
  Virtualization
Power aware data center load balancer
Reduce server
Memcached server

## Slide 130: Core router network processor

## Slide 131: Virtualization
Finding the best configuration for consolidating a set of NPs

## Slide 132: Load adaptive power saving
Cache/Compute replacement on demand
NP/TM/... consolidation on demand

## Slide 133: Datacenter Networking Accelerator (DNA)
Multi Tier Network
Access Ethernet switch
Access Ethernet switch
NIC
PCIe
Mem
CPU
DNA
DNA

## Slide 134: Inside DNA
SerDes interfaces
SerDes interfaces
Mem controller
MAC controller
Gorilla hardware
MAC controller
Mem controller
Ethernet PHY
Ethernet PHY
Memory
Memory
Control processor
Board
FPGA

## Slide 135: DNA applications
Using DNA we can
  Augment the current networks to migrate into openflow - Just an implemnetation, not intersted
  Offload the TCP/IP stack of all access servers into the DNA - Big implementation
  Smart load balancing decision for power saving purpose - Need to study more

## Slide 136: Power aware datacenter load balancer - Related work
Reddi et al., Mobile processors for energy-efficient web search
"[For Microsoft Bing] The Atom is 5x more energy-efficient .... Search queries on Atom encounter higher latencies, different page results, and diminished robustness for complex queries.... Despite these challenges, quality-of-service is maintained for most, common queries [when running Bing on Atom]."

## Slide 137: Power aware datacenter load balancer - Related work
Jingjia Tang et al., The impact of memory subsystem resource sharing on datacenter applications
"We observe performance swings of up to 25% for web search and 40% for other applications based on how application threads are mapped to cores"
Applications
  web search
  bigtable
  content analyzer
  image stiching
  protocol buffer

## Slide 138: Memcached
From Wiki: "Memcached's APIs provide a giant hash table distributed across multiple machines. When the table is full, subsequent inserts cause older data to be purged in least recently used (LRU) order. Applications using Memcached typically layer requests and additions into RAM before falling back on a slower backing store, such as a database"

## Slide 139: Memcached - Popularity
From Wiki: "The system is used by sites including YouTube,[2] Reddit,[3] Zynga,[4] Facebook,[5][6] Orange,[7] and Twitter.[8] Heroku (now part of Salesforce) offers a Couchbase-managed memcached add-on service[9] as part of their platform as a service. Google App Engine, AppScale and Amazon Web Services also offer a memcached service through an API.[10][11][12] Memcached is also supported by some popular CMSs such as Drupal,[13] Joomla, and WordPress.[14]"

## Slide 140: Memcached - usage example
function get_foo(int userid) { /* first try the cache */ data = memcached_fetch("userrow:" + userid); if (!data) { /* not found : request database */ data = db_select("SELECT * FROM users WHERE userid = ?", userid); /* then store in cache until next get */ memcached_add("userrow:" + userid, data); } return data; }

## Slide 141: Memcached accelerator
SerDes interfaces
MAC controller
Gorilla hardware
Ethernet PHY
Soft processor
Mem controller
Memory
Board
FPGA
Mem controller
Memory
Mem controller
Memory
Mem controller
Memory

## Slide 142: Potential Papers
Gorilla and network processor [FPGA2012]
Power on network processors-submit to ANCS
Hardware modleing using Gorilla methodology-submit on DAC
Comparing FPGA/ASIC/processor based version of network processing-submit on ASPLOS/MICRO : Where does the performance come from
Data center networking accelerator
Memcached

## Slide 143: Derek's Comments
Good, I think basing the thesis on applications using Gorilla is good
You should do a complete, non-trivial application that really runs and is better than any ASIC or standard processor.
You need to explain why the performance is better
It has to be significantly easier to program
Infrastrucure costs must be reasonable

## Slide 144: Show casing template-base design
Magilla
  Difference:
    Not only engines but also accelerators/pre-processor/post-processor can be programmed using Gorila instructions
    Multiple engines/Engines clustering
    Mulitple frequency domain
Jason Cong DATE 2012 and other StreamIt on FPGA
  Similarity: Design space exploration for both fine-grain as well as coarse-grain architecture parameters
  Different because of shared data

## Slide 145: Design process - goals
Design cost
  major obstacle for specialization
Rare case handling
  Protocol processing
    Control plane/Data plane
Decouple functionality from architecture
  Domain expert/Architect
Eliminate system layers
Common architecture enhancement patterns
Large number of design alternatives
  design space exploration-first order requirements

## Slide 146: Design process - characteristics
Slice the application into fast/slow path based on profiling result
A library of parallelization templates
A compiler for generating
  MT engines
  Pipelined engines
  Instruction based engin
A tool to explore the design space performance parameters in templates

## Slide 147: Design process - contributions
Fast path/slow path slicing process for targeted applications
Decoupling the functionality and architecture of fast path for targeted applications
A library based architecture enhancement patterns

## Slide 148: Related work - System level
Commodity HW packet processing systems
  Routbricks
  Packetshader
NetFPGA
Many-core Memcached
GPU accelerated Dryad LINQ

## Slide 149: Related work - Architecture
Processor architecture
  Network processors
  Heavily threaded architectures (Niagra)
  Many-core (Tilera)
Processor-NIC integration
  On-loading
Customized cores
  Green droid

## Slide 150: Related work - FPGA related
Overlay architectures
Anderson's student thesis for packet processing
Scott haulk

## Slide 151: Related work-Computation model
StreamIt

## Slide 152: Related work - CAD
HLS
Legup
NISC

## Slide 153: Requirement for programability
Change in specification
Change in workload
Amortizing NRE cost
Notes: Justifying that fixed HW can't be the solution. somthing like the frequent change in workload characteristic/specification ....

## Slide 154
QDR lookup
Cluster Engine
Cluster Engine