## Slide 1: Generating Network-attached Accelerators: Methodology and Applications
Proposal for PhD thesis by: Maysam Lavasani
Advisor: Prof. Derek Chiou
Notes: Thanks for coming to my proposal session. The title of my proposal is

## Slide 2: Outline
Problem statement – 3 slides
Solution statement – 4 slides
Detail solution - Gorilla++ – 17 slides
Initial results – 6 slide
Plan for future – 1 slide

## Slide 3: Specialized Hardware
Pros
  Orders of magnitude more energy efficient than general-purpose processors
Cons
  Inflexible
    Solution: FPGAs flexibility
  Hard to design
    Solution for a class of applications: Gorilla++
Notes: I think it is not a secret that the disruption in dennards scaling is one of the main challenges in current micro-preprocessor industry because of the
Damage to processors energy efficiency.
One of the solutions for this problem is using specialized hardware also known as accelerators.

## Slide 4: High-Level Synthesis (HLS)
HLS built around sequential programming model
  Can exploit fine-grain parallelism automatically
  Cannot exploit coarse-grain parallelism automatically
Available solutions
  User assistance/annotations
    Detecting parallelism
    Finding the right micro-architecture mechanism to exploit the parallelism
  Non-sequential programming model

## Slide 5: Targeted Applications
Networking
  IPv4/IPv6 routing, MPLS switching
Big data applications
  Memcached, distributed K-means, distributed PageRank
Common characteristics
Network intensive
Data parallel e.g., packet, request
Access to shared global memory
Irregular control flow
Random memory access
Notes: Networking and data center applications are an important class of applications which can use specialization for improving the energy. Like many other data parallel applications such applications can utilize large number of hardware execution contexts. Since specialization enables better ratio of required resources(both transistors and energy) over unit of throughput we can increase number of execution units for a particular aggregate resource budget and consequently achieve better efficiency.
Our targeted applications have two important characteristics which differentiate them with other types of data parallel architectures, (i)irregularity and (ii)requirement to access shared resources.

## Slide 6: Solution statement

## Slide 7: System-Level Architecture
Rx Fifo
Tx Fifo
FPGA
General purpose core
$
Shared memory/Interconnect
Network
General purpose core
$
Fast path
Slow path
Notes: One solution for the first problem is using a hybrid FPGA/CPU architecture. We can split the application into two parts the part that handles the common requests and the part that handles the uncommon requests. And put only the common case part into the FPGA and let the uncommon case to be handled by the general purpose cores.
However, the second problem, dealing with application modifications, is still here. In a paper we published recently in computer architecture letter we proposed a solution we call In-line accleartion to solve both of these problems.

## Slide 8: Network-Attached Accelerator
Rx Fifo
Tx Fifo
FPGA
General purpose core
$
Shared memory/Interconnect
Network
General purpose core
$
Fast path
Slow path
Implemented on FPGA substrate
Composed of design components – data flows in/out
Notes: One solution for the first problem is using a hybrid FPGA/CPU architecture. We can split the application into two parts the part that handles the common requests and the part that handles the uncommon requests. And put only the common case part into the FPGA and let the uncommon case to be handled by the general purpose cores.
However, the second problem, dealing with application modifications, is still here. In a paper we published recently in computer architecture letter we proposed a solution we call In-line accleartion to solve both of these problems.

## Slide 9: Gorilla++ Methodology (High-level)
Router: Inport  Classify  QoSCount  Outport
Classify(Input) {
if (Input.protocol == ICMP)
ProcessICMP();
else
Output.port = Lookup();
Output.packet = Input; return Output;}
Classify
QoSCount
Slice
Synthesis
Profile
Classify.backPressure = 0.8
QoSCount.stallTime = 0.75
Refinement rules
FPGA-based accelerator
High throughput
High energy efficiency
Classify(Input) {
if (Input.protocol == ICMP) BailOut();
else
Output.port = Lookup();
Output.packet = Input; return Output;}
Classify_1
Classify_2
QoSCount
Notes: Now that we know the concept of template at high level. We can introduce Gorilla++ methodology. Please know that the description of Gorilla++ methodology is at very high level in order to give an abstract idea of our goal. We will look at the Gorilla++ methodology in more details later and also we see some specific techniques that are the main enablers for this methodology as the contributions of this thesis.

## Slide 10: Thesis Statement
FPGA-based accelerators can improve the performance and energy efficiency of a class of network-intensive applications. Such accelerators can be generated using a design process that facilitates micro-architecture refinements using generic predefined rules.
Notes: This can be done using (i)Automatic Slicing the applications into fast path/slow (ii)a template based design process which enables design space exploration as the first class character in the process for designing the fast path.

## Slide 11: Gorilla++

## Slide 12: History
Magilla - developed in Avici company
  Network processing on FPGA
Gorilla - FPGA2012 paper
  Decoupling the functionality and micro-architecture
Gorilla++ - work in progress
  Composition templates
  Automatic refinement

## Slide 13: Design Components
Design is a hierarchy of components
Composite components
Application specific engines
Infrastructure components - Memory / Cache / Lock engine
Composite component A
Engine component B
Engine component C
Engine component D
Memory components E, F

## Slide 14: Design components – contd.
Component
Notes: In order to present the thesis statement

## Slide 15: Composition Templates
Distributer
Aggregator
Chain
MapReduce
Replicate is an special case for MapReduce
  Divide the work between same components

## Slide 16
Main
Offloaded
Offload
Composition Templates – contd.

## Slide 17: Gorilla++ Development Process
Building base
Micro-architecture
Refining the
Micro-architecture
Slicing
Application Code
Input data
Performance goals
Accelerator Verilog Model
Gorilla++ Methodology

## Slide 18: Gorilla++ Development Process
Building base
Micro-architecture
Refining the
Micro-architecture
Slicing
Application Code
Input data
Performance goals
Accelerator Verilog Model

## Slide 19: Gorilla++ Application Code
Application Code
Input data
Performance goals
Slicing
Building base
Micro-architecture
Refining the
Micro-architecture
Accelerator Verilog Model
Structured dataflow graph of computation engines
Composition code: Scala
  Dataflow connectivity graph
Engines code: Stylized C
  Engine state machine

## Slide 20: Composing a Network Processor (NP)
#pragma INPUT NP_EthIPv4Header_t
#pragma OUTPUT NP_EthIPv4Header_t
#pragma OFFLOAD(lookup, uint32_t, uint8_t)
#pragma STATELSS
GS_ParseEthernet() {/*Body of processing step*/}
GS_ParseIPv4() {/*Body of processing step*/}
GS_LookupOutPort() {/*Body of processing step*/}
GS_UpdateQoS() {/*Body of processing step*/}
GS_UpdatePacketFeilds() {/*Body of processing step*/}
GS_Exception() {/*Body of processing step*/}
val IPv4Engine = Engine(“IPv4.c”)
val Lookup = Engine(“Lookup.c”)

## Slide 21: Composing a NP – contd.
val IPv4Engine = Engine(“IPv4.c”)
Lookup
IPv4
Load balancer
Arbiter
Load merger
IPv4
val HighPerformanceIPv4 = Replicate(IPv4, count=2)
val Lookup = Engine(“Lookup.c”)
val HeaderProcessor = Offload (Replicate(IPv4Engine, count=2), Lookup)

## Slide 22: Composing a NP – contd.
  val Gorilla_NP = MapReduce (Disassembler,
  (SeqReorder (HeaderProcessor),
  PassBuffer), Assembler);
Disassembler
Seq
Header processor
Reorder
Assembler
Pass Buffer
(Chain (Seq, HeaderProcessor, Reorder),

## Slide 23: Gorilla++ Slicing
Application Code
Input data
Performance goals
Slicing
Building Base
Micro-architecture
Refining the
Micro-architecture
Accelerator Verilog Model
Profile the engine codes
Marks frequently used instruction traces as hot traces
Replaces all jumps that exit the hot traces with bailout code
User should write appropriate bailout code
For some server applications bailout code is simple to write

## Slide 24: Gorilla++ Base Micro-architecture
Application Code
Input data
Performance goals
Slicing
Building Base
Micro-architecture
Refining the
Micro-architecture
Accelerator Verilog Model
Engine compiler
Pipelined (loop-free CFG)
Multi-threaded
Composition compiler
For engines calls engine compiler
For infrastructure components instantiate them as Chisel component
For composition templates creates enclosing component
Compose components using latency-insensitive interfaces
Use thunks for deferred execution

## Slide 25: Gorilla++ Base Micro-architecture
Application Code
Input data
Performance goals
Slicing
Building Base
Micro-architecture
Refining the
Micro-architecture
Accelerator Verilog Model
Performance counters
Links Backpressure
Engine Stall time
Engine utilization factor
Generic refinement rules
Refine the micro-architecture
Change performance parameters
Restructure the connectivity graph

## Slide 26: Refinement Rules
Target | Predicate | Action | ID
Improve Throughput | Bottleneck engine | Pipeline | 1
 | Bottleneck Engine / stalled on offload | Multi-thread | 2
 | Bottleneck component | Replicate | 3
 | Bottleneck component | Boost frequency | 4
Save Area | Outlined function in engine | Offload | 5
 | Low utilization replicated engine | Reduce replication factor | 6
 | Low thread utilization | Reduce #threads | 7
Combined rules (avoid local maximums) |  | 5, 3, 2 | 8
 |  | 5,1,2 | 10

## Slide 27: Refinement Rules Example
x
y
Predicate
  Assuming that there is a chain relation between components x and y
  If the amount of backpressure on y input is more than a threshold
  No backpressure from any other output/offload port on y
  y is a concurrent safe and order insensitive
Action
  Replace y with REPLICATE(y, count=2)
  Compile/Profile
Objective / side effect
  Increase throughput / increase area , decrease frequency

## Slide 28: Refinement Rules Example – contd.
x
y1
y2

## Slide 29
Extract fast path
Engine/Composition synthesis
Performance evaluation
DSE engine
No
Yes
No
Perform refinement
Goals met?
Possible refinement?
Yes
Manual step
Domain code
Work loads
Performance goals
Base template library
Modify base template or add new micro-architecture refinement or hands off
Micro-architecture refinement library
Process transition
Input dependency
Select/build a base template
Automatic step
Input
Library
Contributions of this proposal

## Slide 30: Initial Results / Plan for Future

## Slide 31: Gorilla-NP Base Component
Disassembler
IPv4 Engine
Assembler
Pass Buffer
Lookup

## Slide 32: Gorilla-NP Refined Template
Disassembler
Assembler
Pass Buffer
Load balancer
IPv4 Engine
Load merger
IPv4 Engine
Lookup Engine
Arbiter

## Slide 33: NP Performance Refinement Map
Chart: 
| Base micro-arch | #threads=2 | Pipeline Lookup | #threads=4 | #IPv4Engines=4 | #IPv4Engines=8 | #IPv4Engines=16 | Hierarchical arbiter | #threads=3
IPv4Engine backpressure | 0.9 | 0.9 | 0.9 | 0.9 | 0.8 | 0.7 | 0.1 | 0.1 | 0.1
Normalized Area | 0.018665 | 0.030759 | 0.034282 | 0.048186 | 0.21279 | 0.41077 | 0.96553 | 1 | 0.80788
Normalized raw throughput | 0.048913 | 0.058065 | 0.054108 | 0.10822 | 0.22613 | 0.45455 | 0.90909 | 1 | 1
Normalized value to maximum

## Slide 34: Manually Refined Designs
Gorilla-NP – FPGA conference 2012
  VHX870T FPGA: 200MPPS throughput (100 Gbps)
    More than 6x performance of 32 Nehalem cores
Memcached accelerator – CAL/Hot Chips 2013
  Xeon+ VHX240T FPGA: 3.2MRPS throughput
    3.6X more energy efficient than base-line Xeon
K-means accelerator – DAC user track 2013
  Performance comparison (work in progress)

## Slide 35: Contributions
Gorilla++ methodology
  Functional composition with Offload to access shared resources
  Multi-threading support in HLS
  Automatic rule-based refinement
Fast path / Slow path slicing
  Hot trace
  Rollback
Gorilla network processor
  Exploration of design space for infrastructure components
Notes: Design space exploration as first order requirement
The process is not completely automated though.

## Slide 36: Comparison to Closely Related Work
 | Main feature(s) | Difference(s)
Architecture-centric HLS (e.g., NISC) | Micro-code generation for datapath | Composition / MT / refinement
Multi-level HLS SDF (e.g, J.Cong DATE 2012) | Compile time scheduling | Offload-MT / variable latency kernels
Streaming-based HDL (e.g., Streams-C) | Sequential nodes connected through streaming pipes | Offload-MT / refinement
Hardware generators (Genesis) | Hardware parameterization | Composition / refinement
Chisel/Bluespec (Bakrak/Arvind) | Modern language features – atomic rules (Bluespec only) | Offload operation-MT / refinement
TRS-based refinement (Arvind) | Automatic refinement through rule combining and rule scheduling | Programming model – Profile-based refinements vs. compile-time
Hardware patterns (Bakrak) | Use common patterns in the design as a based parameterized hardware | Composition / Profile-based refinements
Magilla (Avici) | FPGA-based networking | Composition / refinement
Modern HLS (e.g. Vivado) | Micro-architecture directives | Offload-MT/Refinement

## Slide 37: Future Work
Implement some important refinement rules
  Replicate/Multi-thread/Pipeline/Offload/Combined rules
Add support for multi-stage computation
Compare refinement with a generic optimization algorithm (e.g., hill climbing)

## Slide 38: Evaluation Methodology
Verilog-level simulation / power estimation
Performance
  Throughput
  Energy efficiency: throughput/power
Productivity
  Code conciseness
  Performance refinement map
    Performance improvement just by applying predefined rules

## Slide 39: Gantt Chart
Task/Month | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Composition Functions |  |  |  |  |  |  |  |  |  | 
Implement Page Rank/K-means |  |  |  |  |  |  |  |  |  | 
Implement some important refinement rules |  |  |  |  |  |  |  |  |  | 
Performance refinement map |  |  |  |  |  |  |  |  |  | 
Writing the thesis |  |  |  |  |  |  |  |  |  | 

## Slide 40: Courses
UT Courses | Instructor | Grade
SOC design – Fall 08 | Dr. Jacob Abraham | A
Comp Arch: User/system interplay – Spring 09 | Dr. Mattan Erez | A
Parallel systems – Spring 09 | Dr. Calvin Lin | A
Parallel comp arch – Fall 09 | Dr. Derek Chiou | A-
Communication systems – Fall 09 | Dr. Yin Zhang | A
Microarchitecture – Spring 10 | Dr. Yale Patt | A-
Comp Arch: Parallelism and Locality – Fall 10 | Dr. Mattan Erez | A

## Slide 41: Related Publications
Maysam Lavasani, Larry Dennison, and Derek Chiou. “A Methodology for Leveraging Reconfigurability in Domain Specific Languages" The First Workshop on the Intersections of Computer Architecture and Reconfigurable Logic (CARL 2010), December 2010
Maysam Lavasani, Larry Dennison, and Derek Chiou. "Compiling High Throughput Network Processors“, Proceedings of the 20th ACM/SIGDA International Symposium on Field-Programmable Gate Arrays, Feb, 2012
Maysam Lavasani, Eric Chung, and John Davis. “Synthesizable, Application-Specific NOC Generation using CHISEL”, Design Automation Conference – Designer Track, March, 2013
Maysam Lavasani, Hari Angepat, and Derek Chiou. “An FPGA-based In-line Accelerator for Memcached”, Computer Architecture Letters, May 2013 – Hot Chips, August 2013

## Slide 42: Thank You

## Slide 43: Execution Model
Engine execution model
  A computation kernel is applied on each input data element
  For each input corresponding output data element(s) are generated
  Kernel is composed of a set of processing steps
Control state
Offload component
Notes: Each component has one input, one output, and n offloads

## Slide 44: A Multi-Threaded Engine
Engine
Control state
Offload component
Context memory
Improves performance unless
  Engine becomes bottleneck
  One of the offloaded components becomes bottleneck

## Slide 45: A Pipelined Engine
Increase the throughput
Pipelining caveats
  No backward jumps
  Access to an off-load engine is restricted to a given pipe stage

## Slide 46: Processing Steps
Processing step
  Arithmetic/logic operations
    program input
    context variables
  Call to special purpose offload engines
  Jump logic to next step
instr_addr_t ProcessingStep_1()
{ IP_protocol_t wordx;
//Lookup the destination address
Dport = LOOKUPX(Da);
//Read the TTL and Chksum fields
wordx = MEMX.read(PP, TTL_WORD);
TTL = wordx.TTL;
Chksum = wordx.CHKSUM;
TTL = TTL – 1;
Chksum = Update_chksum(Chksum);
switch (TTL == 0) {
case OK: Next_step = NP_INSTR_EMIT;
default: Next_Step = NP_INSTR_EXCEPTION;
}
}

## Slide 47: High-Level Synthesis (HLS)
while (true) {
if (InputPacket.newPacket) {
packet=Parse(InputPacket);
OutputPacket=Update(packet);}}
InputPacket
OutputPacket
HLS

## Slide 48: Annotating High-Level Synthesis
while (true) {
if (InputPacket.newPacket) {
packet=Parse(InputPacket);
OutputPacket=Update(packet);}}
Set_directive_dataflow
OutputPacket
InputPacket
HLS

## Slide 49: Data-flow High-Level Synthesis
Input Parse()  Update()  Output
OutputPacket
InputPacket
HLS

## Slide 50: SDF Module Selection / Transformation
Integer linear programming solver
Synchronous Data-Flow
  No side-effect
  Constant delay for computation nodes
  Predetermined number of in/out tokens
Parse Update

## Slide 51: Accelerators Flexibility Challenge
Chart: Energy Efficiency Normalized to General Purpose CPU (Operations/Joule)
 | 8 | 9 | 11 | 30 | 31 | 50 | 90 | 600 | 1010 | 1040 | 1060 | 1100
Merit of specialization
FPGA TAX
The energy efficiency of twelve different designs published in ISSCC conferences (ISCA keynote 2012 – Justin Rattner)
Projected energy efficiency on FPGA substrate (not a real data)
More specialization
ASIP/DSP
ASIC
Quantity
Application changes
FPGA-based accelerators? (for the target applications)

## Slide 52: What Gorilla++ is not?
A new model of computation
  Communicating Sequential Processes (CSPs)
Dead-lock free

## Slide 53: Accelerator Substrates
ASIC accelerator
  Large market size
  Well established standard and protocol
ASIP accelerator
  Can handle application changes
  Same substrate for different applications
FPGA accelerator?
  Less efficient than ASIC (FPGA overhead)
  Hard to program
  Fully flexible
    application changes
    smaller market size

## Slide 54: FPGA-based Accelerators
What if the merit of specialization > FPGA overhead?
What if we can program the FPGAs like software?

## Slide 55: Iterative Micro-architecture Refinement
A set of generic predefined rules
Work on the graph of compositions
Look at the components performance counters
  Templates hide some performance counters in the design
Find potential bottleneck / source of inefficiency
Change parameters and/or
Rewrite the graph of compositions

## Slide 56: Gorilla++ Programming Environment
Concise programming model
  Engine template
  Composition functions
Engine compiler
  Accepts stylized C code
  Written using ANTLR
Composition functions
  Accepts Chisel code
  Written in Chisel/Scala
    Object-oriented
    Functional

## Slide 57: Programming an Engine
Engine
Functionality = “IPv4HeaderProcessing.c”
MicroArchType = MultiThreaded
InputType = PacketHeader_t
OutputType = PacketHeader_t
Offloads = [lookup1, lookup2]
NumOfThreads = 2
Scheduler= RoundRobin
InputStyle = MemoryMapped
ConcurrentSafe = true
OrderSensitive = false
PerformanceCounting = True
Notes: In order to present the thesis statement

## Slide 58: Programming Constructs
Engine template
  Primitive, domain specific, programmable template
  One of the parameters is the functionality as C code
Composition function
  Accepts templates as arguments
  Generates a composite template

## Slide 59: Processing Steps
Processing step
  Arithmetic/logic operations
    program input
    context variables
  Call to special purpose offload engines
  Jump logic to next step
instr_addr_t ProcessingStep_1()
{ IP_protocol_t wordx;
//Lookup the destination address
Dport = LOOKUPX.search(Da);
//Read the TTL and Chksum fields
wordx = MEMX.read(PP, TTL_WORD);
TTL = wordx.TTL;
Chksum = wordx.CHKSUM;
TTL = TTL – 1;
Chksum = Update_chksum(Chksum);
switch (TTL == 0) {
case OK: Next_step = NP_INSTR_EMIT;
default: Next_Step = NP_INSTR_EXCEPTION;
}
}

## Slide 60: Performance Counters
Performance counters are hidden in templates
Engine utilizations
Link utilizations
Input / Output backpressures
Offload backpressures
Offload stall time
Efficiency
  Arbiters
  Schedulers

## Slide 61: Infrastructure Components
Memory structures
  Multi-bank scratch pad – high frequency
Interconnect
  Time (de)multiplexer
Synchronization
  Lock table
Arbiters
Load balancers/mergers

## Slide 62: Deterministic Resource Planning?
SDF-based solutions
  Consider worse case latency for elements
    Not the optimized solutions
  Contention is not considered
  Imperfect components schedulers/arbiters
Deterministic methods can be a complement

## Slide 63: Offload as a SDF with Loop
SDF: compile time scheduling
  Fixed latency
  Pure-functional
  Loop free
    Extensions made to support feedbacks
Gorilla++: improves the designer productivity
  Area-frequency-throughput-latency
Offload can be modeled as a SDF with loop
  But, offloading and multi-threading are important enough to be first order constructs
    More efficient micro-architecture
    More effective refinement rules

## Slide 64: Safety of Composition
User specifies the characteristics of primitive components
  Ordered
  Concurrent safe
Safety in base template – programmer’s responsibility
Safety for refinements
  Every refinement has a safety caveat
    E.g., Only replicate the concurrent safe
    Loop-free dependency graph
Not a new model of computation
  An alternative for traditional HDL for a class of computations

## Slide 65: Refinement Selection Algorithm
Prioritize some refinements
  Combined refinements
Select the objective with largest gap with the goal value
  Apply the refinement
    Highest priority
    Target the objective

## Slide 66: NP Design Space Explorations
Complexity backfires
  Smart thread scheduler
  High-frequency packet memories
  Smart arbiter (RR vs. Opportunistic-fair)
Support for irregularity has cost

## Slide 67: Gorilla/CPU Gap
No instructions
Registers (number of registers/ports)
Customized data-path
  Single-clock packing
  Width
  Pipelining
Customized number of threads/engines
Packet FIFO (not specific to FPGAs)
Customized interconnect
Offloaded operations (not specific to FPGAs)
No speculation/forwarding/renaming

## Slide 68: Timing-insensitive Interfaces
Input data
Input valid
Input ready
FifoIO
Request
Reply
OffloadIO
Meta data
Notes: Mix this with Chisel code

## Slide 69: A Programmable Engine
Context memory
Control state
Offload engine
Off-chip Memory
Engine

## Slide 70: Scaling Throughput
Engine
Multiple engine contexts
  Multi-threaded engines
  Multiple engines
Contexts increase performance until an offload engine becomes the bottleneck
Control state
Offload engine
Off-chip Memory
Context memory

## Slide 71: Multi-threaded Engine Micro-architecture
Engine
Read context
-Execute
-Requests to offload interfaces
-Jump
-Context Edit
Packet memory helper
Engine source bus
Engine sink bus

## Slide 72: Related Work
FPGA-based Accelerators
Network Intensive Processors
High-Level Synthesis / Hardware generators
HPC
Gene sequencing
Signal processing
Simulation
Flat HLS
-Generic HLS with directives
-Pipeline makers
Multi-level HLS
-Language support
-Directive
NetFPGA
Database acceleration
High-frequency trading
Spatial computing
Overlay architectures
Multiple personality
Profile-based offloading
Hardware generators
-Parameter-based (Genesis/Chisel/Bluespec)
-Composition (Chisel/Bluespec)
-Refinement
-TRS-based (Term Rewriting System)
-Algorithm/HW co-design (Spiral)
Architecture centric HLS
Hardware patterns
Magilla
Network processors
Notes: There are research on FPGA accelrators, In-line accelerators, and HLS. We focus on the intersection of these three

## Slide 73: Criteria for using Accelerators
Large market size (quantity)
Large enough portion of apps amenable to acceleration
Merit of specialization (accelerated part) is large
Limited communication between ACC and GPC
Enough area resources for implementing accelerator
Accelerated part requires limited/no changes
  Need flexibility in accelerator to handle changes
Accelerators
General purpose cores
Application A
Application B

## Slide 74: Internet Core Routers
  Multi-chassis system
  322Tbps aggregate bandwidth
  Download the entire Library of Congress content < 1 sec
  Simultaneous video calls for everyone in China
  Specialization in various levels
    Computation
    Memory
    Input/output
CISCO CRS-3 (Carrier Routing System)
1GIPS < 0.1Watts
Independent threads
>10X efficiency over CPU
Notes: GPU: 0.2 GFLOPS/Watt
CPU: Peak 0.3 GIPS for networking it is 1 GIPS
Internet routers are a successful practice in customization with respect to computation, memory, and IO resources. Lets briefly look at the Internet routers architecture which is my role model in this research.
The highest capacity router I could find
  2.73 Watts per Gbps (total power)
  Compute power : 35%

## Slide 75: Benefits of Customization
Figure is from ISCA 2012 Keynote by Justin Rattner
Notes: This graph shows energy efficiency of 20 different fabricated chips which have publication in ISSCC before 2000. The graph is not implementation of single application using different substrate. The efficiency is based on the max throughput of chip among different benchmarks. The operation is basic ALU operation for that particular chip.

## Slide 76: A Composition Function
def Offload (a: (gComponentMD, () => gComponent),
b: (gComponentMD, () => gComponent),
offPort: String) = {
val res = () => new gOffloadedComponent // arguments are not shown
val (left, right) = a._1.offloadDataGen.span( _._1 == offPort)
val restOfOffloadedDataMain = { if (right.isEmpty) left else left ++ right.tail}
val offoff = mergeOffloads(restOfOffloadedDataMain, b._1.offloadDataGen)
(new gComponentMD(a._1.inDataGen, b._1.outDataGen, offoff), res)
}

## Slide 77: A Composition Function – contd.
class gOffloadedComponent extends gComponent
//arguments not shown (main, off, offPort)
{
//…Find the result offloaded interfaces,, put it in offoff variable
io += offoff
io.in <> main.io.in
io.out <> main.io.out
//…mainOff is the offload interface of the main component
for ((n, i) <- mainOff.elements) {
if (n != "in" && n != "out" && n == offPort) {
i.req <> off.io.in
i.rep <> off.io.out
} //if
} // for }

## Slide 78: Routing Experimental Results - 100MPPS on Virtex-6 VHX380T

## Slide 79: Routing Experimental Results - 200MPPS on Virtex-7 VHX870T

## Slide 80: Generating Memcached Accelerator
Update
Retrieval
Remove
s
t
t
Template-based HLS
Slicer
Retrieval
Remove
Memcached 1.4.10
Threading model: Libevent
10687 LOCs
Hot trace: ~ all Get ops
Hot routines LOCs: 963
Hot instructions: <2000
Roll back code: 30 LOCs
Mem Annotations:22 LOCs
57 complex states
Each 1-30 clock cycles
e.g., IP/UDP parsing: 4 states
Notes: We applied this methodology on Memcached. Memcached has 10687 lines of code.
It is using libevent and as the result it has the threading model that we want.
After passing the memcached through the slicer, it is not a surprise that the hot trace
Contains most of the get operations on top of UDP. Get operations that hit expired item is not in the hot path.
The hot routines contains only 963 lines of code and hot instructions are only 2000 static instructions.
The roll back code is only 30 lines of code and there are few lines of code for annotating the memory types.
And then we pass the hot trace plus the rollback code to the HLS tool and generate the hardware.
The generated hardware has 57 FSM states. I should mention that each state is performing large set of operations and for example parsing the IP and UDP is done in 4 steps.

## Slide 81
Engine / composition compilation
Performance evaluation
Design space explorer
No
Yes
No
Perform refinement
Goals met?
Possible refinement?
Yes
Manual step
Accelerator code
Work loads
Performance goals
Add new micro-architecture refinement or hands off
Micro-architecture refinement library
Process transition
Input dependency
Build a base template
Automatic step
Input
Library
Synthesis

## Slide 82: Fast Path Performance/Power
Chart: Offered load K Gets/sec
| 100 | 200 | 400 | 800
1x Xeon core | 100 | 175 | 175 | 175
2x Xeon core | 100 | 200 | 350 | 350
1x Accelerator engine | 100 | 200 | 400 | 590
2x Accelerator engines | 100 | 200 | 400 | 800
8 Watts, 175K RPS, 21.8 Reqs/J
1 Watt, 590K RPS, 590 Reqs/J
27x more energy efficient
Xeon frequency: 2.2 Ghz
FPGA frequency: 100 Mhz
Xeon core performance from Langsto el al., “Enhancing the scalability of Memcached”
Xeon power breakdown: McPAT, FPGA power: Xilinx xPower
64 bytes items
Notes: In this graph we compare the accelerator performance with the best software implementation which is heavily tuned by Intel on top of Xeon processor.
We are showing the performance for one and two inline accelerator engine. And one and two Xeon cores.
X axis is the offered load and Y axis is the sustained throughput. We can see that single accelerator engine can deliver 590 thousand requests per second while consuming only one watt and the Xeon core can deliver 175 thousand requests per second while consuming eight watts.
This translates into 27X energy efficiency gap between the accelerator and the Xeon core.
Please note that this experiment only contains the fast path operations that all can be handled using FPGA.
But what we are really interested is the real work load with slow path as well as fast path operations when there is a overhead for bail out, synchronization between fast path and slow path, and cache coherency overhead.

## Slide 83: Simulation Environment and Parameters
Alpha core single-issue In-order/4Ghz
$
2 MB LLC
Update
Retrieval
Remove
s
t
t
Network
Linux 2.6.38
MCBlaster
Linux 2.6.38
Fast path extension
to NIC state machine
(NS DP83820)/100Mhz
Alpha core single-issue
In-order/4Ghz
Full system stack cycle-accurate simulation using Gem5 simulator
  Populate phase: one million items before test
  Measurement: throughput based on 1ms time out
1Gbits/s
Client
Server
Notes: In order to measure the performance of in-line accelerator cooperating with general purpose core,
We spent a good deal of time to simulate the full system stack of both client and server system in Gem5 environment. We changed the server NIC model and added the fast path state machine to NIC state machine.
On the client we are running mcblaster and on the server we are running original memcached with some changes in libc library.

## Slide 84: Hybrid Architecture Performance
Xeon core performance from Langsto, et al. “Enhancing the scalability of Memcached”
64 bytes items
Chart: Slow path operations: K Sets/sec
| 0 | 10 | 15 | 20
 | 583 | 440 | 423 | 400
Xeon core: 175K Gets/sec
Single Engine Accelerator Throughput
Notes: And this is the performance of a hybrid FPGA/general purpose core when we have both slow path operations which are the set operations as well as the fast path operations which are the get operations.
The X axis is the different set operation rates and the Y axis is the maximum throughput for single engine.
As we see having some slow path operations mixed with fast path operations degrades the performance of the system. However we still far higher than Xeon core pure Get performance and of course the big win is the gap between the power consumption of these two hardware.

## Slide 85: Accelerated Memcached throughput

## Slide 86: Board Implementation
Gorilla-generated network processor
IPv4 only on ML605
  Xilinx Virtex-6 XC6VLX240T
  Emulate QDRs with accurate timing in BRAMs
16-3-2 configuration delivers 100MPPS
  Most of the logic running at 100Mhz
  Consistent with simulation results
Random packet generator and statistics collector
Core power (excluding the I/O) less than 4 watts
Notes: A picture from board required here

## Slide 87: Kmeans Accelerator
Val KmeansPipe =
PIPELINED_ENGINE(“kmeans_pipe.c”)
Val KmeansDataFeed =
MT_ENGINE(“Kmeans_control.c”)
Val KmeansCoresCluster =
REPLICATE(OFFLOAD(
KmeansDataFeed, KmeansPipe), coreCounts,
reduce = kmeansReducer)
Val Kmeans_accl =
Offload(Streamer, KmeansCoresClusters)

## Slide 88: Timing-insensitive Interfaces
Input data
Input valid
Input ready
FifoIO
Request
Reply
OffloadIO
Meta data
Notes: Mix this with Chisel code

## Slide 89: Component
Component
Notes: Mix this with Chisel code

## Slide 90: Definition of Back-pressure
On a given interface back-pressure happens if the number of cycles that valid signal is one and ready signal is zero is larger than a threshold (T1 threshold)

## Slide 91: Definition of Bottleneck
An engine is bottleneck if it back-pressures on the input and not back-pressures on the output or any request side of the offload interfaces

## Slide 92: Definition of Offload-inefficient
An engine is offload-inefficient if the ratio of offload time in at least one of the offload interfaces over the total computation time is higher than a threshold (T2 threshold)

## Slide 93: Refinement Rules
Rule 1
Pred-1:Is there any engine that is bottleneck
Pred-2:Is the CFG of the engine loop-free?
Action: pipeline it
Rule 2
Pred: Is there any engine that is offload-inefficient
Action: multi-thread it

## Slide 94: K-means Domain Code
K-meansEngine() {
//OUTPUT Point_t; INPUT Point_t;
Int closestId;
Distance_t centers[n], distances[n], closestDistance;
closestDistance = INFINITI;
for (i=0; i<n; i++) {
float c = center[i];
float d = distance (input, c);
if (d < closestDistance) closestDistance = d;
closestId = i;} //end of for loop
distances[closestId] += closestDistance;}
Engine(“k-means.c”)
distance

## Slide 95: Distance Function
Point_t distance(Point_t p1, Point_t p2) {
output = sqrt(sqr(p1.x-p2.x), sqr(p1.y- p2.y), sqr(p1.z-p2.z))
}

## Slide 96: Offload Maker Operation
Objective: If there are enough Heavy operations in a CDFG sub-graph outline it (outlining is a compiler technique)
  Memory operations
  Floating point operations
Make a new offloaded engine
  The input/output are the packed input/output arguments of outlined function
  The offloaded interfaces are the set of offloaded interfaces in the outlined code

## Slide 97: K-means Original Engine
Engine(“k-means.c”)
distance
Distance:
    Request side is two ThreeDimFloat
Reply side is on ThreeDimFloat
Output = sqrt(sqr(in1.x-in2.x), sqr(in1.y-in2.y), sqr(in1.z-in2.z))
Notes: Mix this with Chisel code

## Slide 98: Intra Engine Parallelization Patterns
Pipelining
Multithreading

## Slide 99: Gorilla Compilation Process
Written in ANTLR

## Slide 100: Packet Header Processing

## Slide 101: In-line Acceleration in Core Routers
Throughput machines
IO intensive
Irregularity in control-flow
High bandwidth random memory accesses
Customization at various levels
  Network interfaces
  Inter-core communication
  Memory interfaces
  Core architecture
Network processor
Interconnect
Memory
Slow-path processor
Metro NP (CRS-1 2007)
                188 32-Bit embedded RISCs
                96Gbps bandwidth
Line card
Notes: We show a simplified view of a router architecture.
Fast-path accelerator = Data-plane accelerator = In-line accelerator
FCRAM: Fast cycle RAM: more aggressive pipelining on handling DRAM commands

## Slide 102: FPGA Overheads
From: H. Wong et al, “Comparing FPGA vs Custom CMOS and the Impact on Processor Microarchitecture”, FPGA 2011
Notes: Unlike ASICs, FPGAs are a highly flexible substrate for specialization. However they have the area and timing overhead of building logic, memory, and interconnects through programmable components.
An important question is whether the benefit of customization can out weight the FPGAs overhead?

## Slide 103: GPP-ASIC Gap
Reconfigurable components for application-specific processor architectures, Nolll, T et al.
Five orders of magnitude gap

## Slide 104: GPP-ASIC Gap
Understanding the source of inefficiencies in general-purpose chips, ISCA 2010, Horowitz. M. et al.
Notes: Pentium 4 with SSE 2.8Ghz

## Slide 105: Gorilla++ Methodology (High-level)
Router: Inport  Classify  CountQoS  Outport
Classify(Input) {
if (Input.protocol == ICMP) ProcessICMP();
Lookup(); return Output;}
Classify();
QoSCount();
Slice
Build base template
Synthesis
Profile
A.backPressure = 0.8
B.stallTime = 0.75
Refinement rules
FPGA-based accelerator
High throughput
High energy efficiency
A
B
Router: Inport  Classify  CountQoS  Outport
Classify(Input) {
if (Input.protocol == ICMP) BailOut();
Lookup(); return Output;}

## Slide 106: Gorilla++ Methodology (High-level)
Router(Input) {
if (Input.protocol == ICMP) ProcessICMP();
Classify();
return Output;}
process();
Generate();
RouterFastPath(Input) {
if (Input.protocol == ICMP) Bailout();
Classify();
return Output;}
Slice
- Select a base template
- Refactor the code
Synthesis
Profile
A.backPressure = 0.8
B.stallTime = 0.75
Refinement rules
FPGA-based accelerator
High throughput
High energy efficiency
Profile
A
B

## Slide 107: Accelerators Flexibility Challenge
Rarely used accelerators not justifiable
Part of specialization is traded for some flexibility
  Cover larger set of computations
  Amortize the cost of specialized hardware
Achieve flexibility using FPGAs
  Lower performance than ASIC but high flexibility
  FPGA-based network-attached accelerators?
Notes: When we do not build a customized hardware for a computation? (i) Not fit into hardware (ii) Not used frequent enough

## Slide 108: Accelerators Design Challenge
Design challenges for accelerators
  Complex hardware design/verification process
    FPGA-based hardware requires very efficient micro-architecture
  Both domain expertise and hardware knowledge
High Level Synthesis
  For complex designs, designer assistance is required
    Large number of HLS directives
  Reduce/eliminate directives for the target accelerators?

## Slide 109: Flexibility Challenge for Accelerators
ASICs: specialization  less flexibility
  Covering smaller variety of computations
  Demanded quantity of accelerator is high  works
  Demanded quantity of accelerator is not high enough  problem
    Cost of the specialization not justifiable
    Buy back some flexibility to cover more computations
FPGAs: both specialization and flexibility
  FPGA overhead
  Less efficient than ASIC
Merit of specialization > FPGA overhead?
    FPGA-based accelerator for target applications

## Slide 110: Design Challenge for Accelerators
HLS (High-Level Synthesis) quality of results
  Less efficient than hand-designed micro-architectures
    Efficient micro-architectures: exploits different types of parallelisms
    Conventional HLS: exploits only few types
  Designer provides micro-architecture: Architecture-centric HLS
  Designer provides hints about micro-architecture: Modern HLS tools
  Start from non-sequential programming model: e.g., SDF
    Regular computation
A methodology to improve designer’s productivity?
  Exploits different parallelization opportunities automatically
  More generic applications than SDF

## Slide 111: Scaling the Performance - Projection
Projecting the performance of Xeon + In-line accelerator
  Assumes unused cores can be clock gated
  Almost the same 3.15M reqs/sec throughput as dual package configuration
    Eight engines (fast path) + single Xeon core (slow path) + Xeon un-core
    3.6X more energy efficient
Chart: Power (Watts)
| 22.4 | 31.6 | 50 | 86.8 | 173.6
Xeon | 175000 | 350000 | 700000 | 1400000 | 3150000
Xeon + In-line accelerator | 400000 | 800000 | 1600000 | 3200000
Network: 30% (3G bits/sec)
FPGA area: 40% (69600 LUTs)
Memory BW: 2.3% (1.15G bytes/sec)
Number of cores/engines is labeled for each data point
Two Xeons
Scaling the Performance - Projection
Notes: To study the design space of adding our automatically generated hardware accelerator engines to an existing system, we designed a model of incrementally adding engines to a baseline Xeon-based system
In this figure I am showing power vs. throughput of a Xeon processor as well as the projected power vs. throughput of a Xeon processor + an in-line accelerator.
The Xeon performance and power is reported from Intel experience. And as you see the performance scales linearly with number of cores.
For the system with in-line accelerator we are assuming that we have FPGA resources as big as the Virtex-6 part we saw before. We are also assuming that we can power gate the Xeon cores except one for processing slow path operations.
As you can see using 8 engines we can deliver almost the same performance as two processors performance. However, we can save a lot of power and improve the energy efficiency by 3.6x.
We still have scaling headroom in terms of network and memory bandwidth, as well as FPGA resources, allowing for larger configurations with equal power budgets rather than equal performance.